# OY-RPJ

## Engine start

Seatbelts	Locked

Cabin doors	Closed

Parking brake	Set

Lights and pitot heat	Off

Avionics	Off

Circuitbreakers	Check

Carburator heat	Off

Fuelselector	Rotate,then both

Mixture	 Rich

Throttle	1 cm

-----------------------------------------------------------

Masterswitch	On

Fuelquantity	Check

Rotating Beacon	On

Navigationlights	As req.

Prime as req.	 Primer locked

Propeller area	Clear

-----------------------------------------------------------	Engine…………………………………….	Start

Oilpressure………………...	OK within 30 sec.

Throttle……………………….…….	1000 RPM

-----------------------------------------------------------

Flaps………………………………………...	Up

Avionics……………………….…………….	On

Radio selector panel………………………	Set

Gyrocompas……………………………….	Set

Altimeter…………………………….……...	Set

Parking brake………………………………	Off

Taxilight……………………………………..	On

## Taxi

Brakes…………………………………..	Check

Flight instruments……………………...	Check

## Before Take off

Taxilight……………………………………..	Off

Parking brake……………………………...	Set

Altimeter………………………………..	Check

Fuelselector………………………………	Both

Trim………………………………	Check & set

Flaps……………………………...	Check & set

Flight controls…………………….……	Check

-----------------------------------------------------------

Throttle………………………………	1700RPM

Magnetos….(Max 125/50)……………	Check

Carburator heat………………………..	Check

Engine instruments……………………	Check

Suction……(Min 4,6 – Max 5,4)…….	Check

Ampér meter…………………………...	Check

Throttle……………………………...	1000RPM

-----------------------------------------------------------

Navigation aids……………………….	As req.

Departure briefing	Complete

Landing light………………………….…….	On

Parking brake………………………………	Off

## Line up

Pitot heat	On

Transponder	Position ”Alt”

Gyrocompas	Set to runway

Compas	Check with runway

Vr	60mph

Vx	68mph

Vy	90mph

Enroute climb.	90mph

# Climb	.

Flaps	Up

Landing light	Off

Altimeter..(If above T.A.)	Set

### Cruise

Throttle	Set

Mixture	Set

Gyrocompas	Check

Fuelselector	L,R or Both

# Before descend	.

Fuelselector	Both

Mixture	Enrichen as req.

Gyrocompas	Check

VFR

Approach speed.	80mph

Threshold speed with full flaps	70mph

IFR

Holding speed	100mph

Beacon outbound	100mph

Beacon inbound	100mph

Before landing	.

Approach briefing	Complete

Landing light…..	Consider

Altimeter	Check

Gyrocompas	Check

-----------------------------------------------------------

Mixture	Rich

Carburator heat	On

Flaps	Set

After landing	.

Flaps	Up

Carburator heat	Off

Pitot heat	Off

Transponder	Off

Landing light	Off

Taxilight	On

# Parking	.

Parking brake	Set

Taxilight	Off

Avionics	Off

Mixture	Idle cut-off

Rotating beacon	Off

Magnetos	Off

Masterswitch	Off

Controls	Lock