PA28 CADET EMERGENCY CHECKLIST

ENGINE FIRE ON GROUND

ENGINE NOT YET RUNNING

1. STARTER....................................................ENGAGE

2. MIXTURE .........................................IDLE CUT OFF

3. THROTTLE.......................................................OPEN

CONTINUE WITH “ON GROUND EMERGENCY

CHECK LIST”

ENGINE IS RUNNING

1. FUEL SELECTOR...............................................OFF

2. THROTTLE.......................................................OPEN

WHEN FIRE STOPS CONTINUE WITH “ ON GROUND

EMERGENCY CHECK LIST”

ON GROUND EMERGENCY

1. FUEL SELECTOR...............................................OFF

2. MIXTURE .........................................IDLE CUT OFF

3. BATTERY/ALTERNATOR...................................OFF

4. MAGNETOES......................................................OFF

5. PARKING BRAKE ................................................ON

6. EVACUATE AIRCRAFT

7. IF FIRE .................................................EXTINGUISH

ENGINE FAILURE

DURING TAKEOFF RUN

1. THROTTLE..................................................CLOSED

2. BRAKES................................................SUFFICIENT

IMMEDIATELY AFTER TAKE-OFF

1. SPEED...........................................................73 KTS

2. FLAPS...............................................AS REQUIRED

FLY THE AIRCRAFT

DURING CRUISE

1. FUEL SELECTOR...........................CHANGE TANK

2. STBY FUEL PUMP...............................................ON

3. SPEED...........................................................73 KTS

4. CARBURETOR HEAT..........................................ON

5. MIXTURE...........................................................RICH

6. PRIMER.......................................................LOCKED

7. MAGNETOS.....................................................CHKD

IF NOT RESTORED, CONTINUE WITH FORCED LANDING CHECK LIST

ENGINE FIRE IN FLIGHT

1. FUEL SELECTOR...............................................OFF

2. FUEL PUMP........................................................OFF

3. THROTTLE.......................................................OPEN

4. HEATER AND DEFROSTER..............................OFF

WHEN FIRE STOPS

5. MIXTURE..........................................IDLE CUT OFF

CONTINUE WITH FORCED LANDING CHECK LIST

FORCED LANDINGS

EMERGENCY LANDING WITHOUT ENGINE POWER

1. FUEL SELECTOR...............................................OFF

2. MIXTURE .........................................IDLE CUT OFF

3. BATTERY/ALTERNATOR...................................OFF

4. MAGNETOS........................................................OFF

5. SEAT BELTS..............................................TIGHTEN

ELECTRICAL FAILURE

ALT ANNUNCIATOR LIGHT ILLUMINATED

1. AMMETER.................................CHECK TO VERIFY

2. IF ZERO...............................ALTERNATOR TO OFF

3. REDUCE ELECTRICAL LOADS TO MINIMUM.

4. CIRCUIT BREAKERS.....................................RESET

5. ALTERNATOR......................................................ON

6. IF NOT RESTORED..................ALTERNATOR OFF

7. THE BATTERY IS NOW THE ONLY SOURCE

ELECTRICAL FIRE IN FLIGHT

1. BATTERY/ALTERNATOR...................................OFF

2. ALL OTHER SWITCHES.....................................OFF

3. VENTS..............................................................OPEN

4. CABIN HEAT.......................................................OFF

EXTINGUISH THE FIRE. AS A LAST RESORT USE THE FIRE EXTINGUISHER. VENTILATE AFTERWARDS AND LAND AS SOON AS POSSIBLE.

IF POWER IS NECESSARY FOR COMPLETION

1. BATTERY MASTER..............................................ON

2. CIRCUIT BREAKERS…...................................CHKD

NOW TURN ON NECESSARY EQUIPMENT ONLY, ONE AT THE TIME, WITH DELAY AFTER EACH

CABIN FIRE

1. BATTERY/ALTERNATOR...................................OFF

2. VENTS/CABIN HEAT..................................CLOSED

EXTINGUISH THE FIRE. AS A LAST RESORT USE THE FIRE EXTINGUISHER. VENTILATE AFTERWARDS AND LAND AS SOON AS PRACTICAL.